## Slide 1: Lagopus: High-performance Software OpenFlow Switch for Wide-area Network
June 2014
NTT Network Innovation Laboratories

## Slide 2: Agenda
Motivation and Target
Development Status
Evaluation
  Conformance
  Performance
Future Development Plan
A bird in cloud

## Slide 3: Motivation
Agile and flexible networking
  Full automation in provisioning, operation and management
  Seamless networking for customers
Server virtualization and NFV needs a high-performance software switch
  Small latency
  Wire-rate with short packet (64B)
NO high-performance OpenFlow 1.3 software switch for wide-area networks
  1M flow rules
  10Gbps-wire-rate
  Management protocol

## Slide 4: Target of Lagopus
High performance software-based OpenFlow switch
  10Gbps wire-rate packet processing
  1M flow rules
Expands the application to wide-area networks
  Not only for data centers
  WAN protocols, e.g. MPLS and PBB
  Various management/configuration interfaces
Open Innovation
  To be released as OSS

## Slide 5: Specific Implementation Target
ONF standard specification support
  OpenFlow Switch Specification 1.3.4
    Multi tables, Group tables support
    MPLS, PBB, QinQ, support
  OF-CONFIG 1.1
Multiple data-plane configuration
  High performance software data-plane on Intel x86 bare-metal server
    Leverages commodity server architecture
  Bare metal switch
    Utilizing switch ASIC
Various management/configuration interfaces
  OF-CONFIG, OVSDB, CLI
  SNMP, Ethernet-OAM functionality

## Slide 6: Agenda
Motivation and Target
Development Status
Evaluation
  Conformance
  Performance
Future Development Plan

## Slide 7: Development status
Performance
  10 GbE wire-rate
  1M flow rules
Function:
  OpenFlow 1.3 agent: well-tested
  OpenFlow 1.3 software data plane: well-tested
  OpenFlow 1.3 switch ASIC data plane: research
Management Interface / protocol:
  CLI: prototype
  SNMP: prototype
  OF-CONFIG: prototype
  OVSDB: research

## Slide 8: Design
Switch agent and data plane component
  Connected via event queue
  Supports multiple data plane implementations
Switch agent
  Modular architecture
  Easy to add configuration and management protocols
Software data plane
  User space implementation using Intel DPDK
  Easy deployment
OpenFlow controller
OpenFlow 1.3

## Slide 9: Software data plane implementation
OpenFlow data plane processing
  Must lookup and modify various protocol header
  Performance limitation of single CPU core processing
Exploit many core CPUs
  Pipelining: dividing I/O and packet processing
  Parallelizing each processing
    Improves performance and reduces I/O overhead
NIC 1
RX
NIC 2 RX
I/O RX
CPU0
I/O RX CPU1
NIC 1
TX
NIC 2 TX
I/O TX
CPU6
I/O TX
CPU7
Flow lookup packet processing
CPU2
Flow lookup packet processing
CPU4
Flow lookup packet processing
CPU3
Flow lookup packet processing
CPU5
NIC 3
RX
NIC 4 RX
NIC 3
TX
NIC 4 TX
NIC RX buffer
Ring buffer
Ring buffer
NIC TX buffer

## Slide 10: Agenda
Motivation and Target
Development Status
Evaluation
  Conformance
  Performance
Future Development Plan

## Slide 11: OpenFlow 1.3 Conformance Status
Conformance test results by Ryu Certification
  http://osrg.github.io/ryu/certification.html
 | OpenFlow Switch | Action (56) | Set Field (170) | Match (702) | Total (928)
Software | OVS (netdev) | 27 | 71 | 433 | 531
 | OVS (kernel) | 17 | 65 | 433 | 515
 | Indigo Virtual Switch | 17 | 46 | 362 | 425
 | ofswitch13 | 41 | 69 | 419 | 529
 | LINC | 24 | 71 | 472 | 567
 | Trema | 49 | 129 | 612 | 790
 | Lagopus vswitch | 56 | 162 | 702 | 920
Hardware | Centec V350 | 6 | 11 | 196 | 213
 | HP 2920 | 0 | 0 | 20 | 20
 | NoviFLow NoviKit200 | 31 | 71 | 399 | 501
 | Pica8 P-3290 | 10 | 27 | 386 | 423

## Slide 12: Performance Evaluation
Summary
  Throughput: 10Gbps wire-rate
  Flow rules: 1M flow rules
Evaluation models
  WAN-DC gateway
    MPLS-VLAN mapping
  MPLS P router
    MPLS label switching

## Slide 13: Performance Evaluation
Evaluation setup
Server spec.
  CPU: Dual Intel Xeon E5-2660
    8 core(16 thread), 20M Cache, 2.2 GHz, 8.00GT/s QPI, Sandy bridge
  Memory: DDR3-1600 ECC 64GB
    Quad-channel 8x8GB
  Chipset: Intel C602
  NIC: Intel Ethernet Converged Network Adapter X520-DA2
    Intel 82599ES, PCIe v2.0
Server
Lagopus
Flow table
Network
tester
Flows
Throughput
Flow
rules
Packet size
Flow
cache
(on/off)

## Slide 14: WAN-DC Gateway Throughput vs packet size, 1 flow, no flow-cache

## Slide 15: WAN-DC Gateway Throughput vs packet size, 1 flow, flow-cache

## Slide 16: WAN-DC Gateway Throughput vs flows, 1518 bytes packet

## Slide 17: MPLS P router Throughput vs packet size, 1 flow, no flow-cache

## Slide 18: MPLS P router Throughput vs packet size, 1 flow, flow-cache

## Slide 19: MPLS P router Throughput vs flows, 1518 bytes packet

## Slide 20: Agenda
Motivation and Target
Development Status
Evaluation
  Conformance
  Performance
Future Development Plan

## Slide 21: Future Development Plan
40Gbps-wirerate high-performance switch
Hypervisor integration
Tunnel processing
High availability
Open source activity

## Slide 22
Thank you for your attention
This research is a part of the project for “Research and Development of Network Virtualization Technology” supported by the Ministry of Internal Affairs and Communications.